## Slide 1: SURFACE OZONE IN URBAN, SEMI-RURAL AND RURAL SITES IN ISTANBUL, TURKEY
Ulas Im1, Selahattin Incecik2, Sema Topcu2, Yurdanur S. Unal2, Tayfun Kindap3, Meltem Guler4, Orhan Yenigun4, Adil Tek5, Mehmet T. Odman6, Mete Tayanc7
1 University of Crete, Department of Chemistry, Environmental and Chemical Processes Laboratory, Greece
2 Istanbul Technical University, Department of Meteorology, Istanbul, Turkey
3 Istanbul Technical University, Eurasia Institute of Earth Sciences, Istanbul, Turkey
4 Bogazici University, Institute of Environmental Sciences, Istanbul, Turkey
5 Bogazici University, Kandilli Observatory and Earthquake Research Institute, Laboratory of Meteorology, Istanbul, Turkey
6 School of Civil and Environmental Engineering, Georgia Institute of Technology, USA
7 Marmara University, Department of Environmental Engineering, Istanbul, Turkey

## Slide 2: Tropospheric Ozone Chemistry
Reactions involving NO2, NO and O2 produce and destroy O3.
Photodissociation of NO2
NO2 + hv  NO + O (1)
and ozone formation
O + O2 + M  O3 + M (2)
and depletion
NO + O3  NO2 + O2 (3)

## Slide 3
Radical formation in the atmosphere from NMVOCs
most important here are the reactions with the hydroxyl radical and more generally the peroxy radical
HO*2 + NO  NO2 + HO* (4)
RO*2 + NO  NO2 + RO* (5)
Thus when NO molecules are consumed, ozone is spared and it accumulates.

## Slide 4
NO reacts with ozone destroying it (rapidly) and regenerating NO2, so the presence of NO will prevent the build up of ozone
Daylight hours: NO, NO2 and O3 equilibrate (photostationary state)
Evening time:fresh inputs of NO from rush-hour traffic without photochemical reactions –depletes ozone-

## Slide 5: O3 production
Net O3 production is expressed as a function of NOx(= NO + NO2) and NMVOC concentrations

## Slide 6
under NOx – sensitive conditions, ozone formation is almost entirely governed by NOx and largely independent of VOCs,
under VOC – sensitive conditions, ozone formation is related to the increase in VOCs and not to NOx changes.

## Slide 7: Understanding of Photostationary State and Impact of NO2 over NOx
j : rate of NO2 photolysis
(solar radiation-angle of sun)
k2 : rate coefficient for the reaction of NO with O3
(ambient temperature)
[Seinfeld and Pandis, 1998; Mazzeo, (2005)]
[O3] = j [NO2]/k2[NO]

## Slide 8: OZONE MEASUREMENTS IN ISTANBUL
Ozone (O3) measurements conducted by Metropolitan Municipality of Istanbul (IBB) since 1999
All urban/traffic stations
Data has been statistically evaluated for different periods in a number of studies (Topcu and Incecik, IJEP, 2002 and FresEnvBull, 2003; Im et al., WASP, 2006; Im et al., AtmRes, 2008)
Generally low O3 levels (mean=~20 ppb) have been reported (Kanakidou et al., AtmEnv Review, 2011)
INTRODUCTION METHODS RESULTS CONCLUSIONS

## Slide 9: MOTIVATION
All stations are urban with low O3 levels due to anthropogenic emissions from traffic in particular
Urban sites may not represent the general O3 profiles in the extended area of a city
Precursor emissions lead to O3 formation downwind of the sources (Kanakidou et al., AtmEnv, 2011, Im et al., ACP, 2011)
O3 levels in non-urban sites should also be investigated
Continuous O3 measurements at different sites with different characteristics (geography, emissions , etc…) are needed
COST728 Action (Incecik et al., COST728 Technical Report, 2010) and TUJJB projects
INTRODUCTION METHODS RESULTS CONCLUSIONS

## Slide 10: SCOPE OF THE STUDY
Establish new measurement sites to monitor non-urban levels of O3 and NOx in Istanbul to investigate:
  seasonal and diurnal variations of surface O3 and NOx
  the weekday-weekend differences
  the regional influences by applying cluster analysis
INTRODUCTION METHODS RESULTS CONCLUSIONS

## Slide 11: STUDY AREA
Istanbul is a megacity with a population of about 15 million
Urban/industrial/traffic emissions
About 2.8 million motor vehicles
More than 80% of CO and NOx emissions and 45% of NMVOC emissions are originated by traffic emissions (Markakis et al, APR, 2012)
Dominant wind direction is southerly in winter and northerly in summer
INTRODUCTION METHODS RESULTS CONCLUSIONS
Annual traffic NOx emissions

## Slide 12: NEW MEASUREMENT SITES
3 new measurement sites have been established in frame of the COST728 Action and TUJJB projects
  Goztepe site (urban/traffic): O3 and NOx measurements
  Kandilli site (semi-rural): O3 measurements
  Büyükada site (rural/island): O3 and NOx measurements
Kandilli
Goztepe
Büyükada
INTRODUCTION METHODS RESULTS CONCLUSIONS

## Slide 13: Büyükada-Prince’s Island
Island station, at the crest (156 m)
No traffic and industry
Shipping and biogenic emissions only
Emission transport from mainland

## Slide 14: Princes’ Island (Büyükada)
The Island has an area of 5,42 km2 with a population of 7320 inhabitants in winter.
no traffic,
the only transport being horse and cart. Motorized vehicles except service vehicles are forbidden.
Measurements of background NO/NO2/NOx and O3 concentrations at the crest of the island. Operated since October 2007

## Slide 15: Göztepe (on Highway)
Represents traffic emissions on one of the major highways.
07:00-21:00 hrs very dense traffic
Connected to the two Bosphorus Bridges
Operated since October 2007

## Slide 16: Kandilli (Bosphorus)
Operated since: 07.09.2007
Low traffic
Semi - urban
Shipping from Bosporus strait

## Slide 17: CLUSTER ANALYSIS
HYSPLIT back-trajectory model
Total of 805 days for the Kandilli station
72-hour periods
1000 m starting height
INTRODUCTION METHODS RESULTS CONCLUSIONS

## Slide 18: HOURLY O3 & NOx VARIATIONS
Surface O3
Surface NOx
INTRODUCTION METHODS RESULTS CONCLUSIONS

## Slide 19: SEASONAL AND DIURNAL O3 VARIATIONS
GOZTEPE
KANDILLI
BÜYÜKADA
INTRODUCTION METHODS RESULTS CONCLUSIONS

## Slide 20: DIURNAL O3 vs. NOx VARIATIONS
Correlation (r) = -0.64 (p=0)
Correlation (r) = -0.54 (p=0)
BUYUKADA GOZTEPE
INTRODUCTION METHODS RESULTS CONCLUSIONS

## Slide 21: WEEKEND EFFECT
Differences are calculated for the ozone-season
Slightly higher O3 levels at weekends at Goztepe (14%)
Opposite pattern at Kandilli (2%) and Buyukada (7%) sites
Differences are not significant
Delay of peak O3 levels at weekends (~1 hr)
Largest difference at Goztepe due to traffic emissions
Differences between weekend and weekday did not exceed 9 ppb at any station
INTRODUCTION METHODS RESULTS CONCLUSIONS

## Slide 22: CLUSTER ANALYSIS
The largest contributions originate from the East Mediterranean and northern Black Sea (~17% each)
Northeasterly and easterly transports contribute by >10%, originating from Eastern Europe and Eastern Mediterranean.
Clusters 11 and 6 represent short range transport and circulating patterns over Istanbul area
Much smaller contributions (<4% ) originate from Eastern Europe, but also from eastern borders of Turkey, North Africa and Balkan region.
INTRODUCTION METHODS RESULTS CONCLUSIONS

## Slide 23: CONCLUSIONS
Clear seasonal variation exhibiting a maximum in summer and a minimum in winter.
Highest monthly and daily O3 mixing ratios were observed during spring and summer.
Higher O3 levels at the rural site compared to the semi-rural and the traffic sites.
The lowest O3 mixing ratios measured at the traffic site (titration effect of local high NOx emissions).
O3 mixing ratios for the weekend days were slightly higher than that on weekdays at the Göztepe site, while opposite holds at the semi-rural and rural sites.
Differences in the time of observed peak O3 and the variability during the rush hours were notable, particularly at the traffic site.
The sharp decrease in the morning rush hour O3 levels during weekdays were not observed in weekends.
Transport is mainly from Europe, Balkans and the Black Sea to Istanbul.
Elevated levels of O3 might be attributed to a mix of transport and local production.

## Slide 25
THANK YOU
Acknowledgements