## Slide 1
Atmospheric Organic Aerosol: More Than Primary Emissions
Brent J. Williams
Raymond R. Tucker ICARES Career-Development Assistant Professor
Washington University in St. Louis
Department of Energy, Environmental, & Chemical Engineering
PI: Atmospheric Chemistry & Technology (ACT) Laboratory
Mumbai: December 7, 2012

## Slide 2
2 main questions to discuss today:
1) Why do we care?
2) Where does it come from?
Organic Aerosol

## Slide 3: Why Do We Care: Size-dependent Health Effects
[NARSTO, 2003]
Course aerosols deposit by impaction in nose and throat.
Ultrafine aerosol deposit by diffusion deeper in lungs in smaller pathways.
Fine aerosol has a minimum in deposition efficiency at approximately 0.5 micron diameter.
Many organic species in Fine PM are classified as toxins, mutagens, and carcinogens.

## Slide 4: Why Do We Care: Climate Effects
IPCC-Climate Change, 2007
Radiative forcing components
Changes since 1750 (preindustrial)
Not accounting for many aerosol indirect effects.

## Slide 5
IPCC-Climate Change, 2007
Sulfate
Primary Organic Carbon from Fossil Fuels
Black Carbon from Fossil Fuels
Biomass burning
Nitrate
Mineral Dust

## Slide 6
IPCC-Climate Change, 2007
Sulfate
Primary Organic Carbon from Fossil Fuels
Black Carbon from Fossil Fuels
Biomass burning
Nitrate
Mineral Dust
Not Accounting for Secondary Organic Aerosol (SOA). Is there enough SOA to make a difference?

## Slide 7
2 main questions to discuss today:
1) Why do we care?
2) Where does it come from?
-primary vs. secondary
Organic Aerosol

## Slide 8
Organic Aerosol is Most Abundant Fine PM Component Globally
Zhang et al., 2007
organics
sulfate
nitrate
ammonium

## Slide 9
Northern Hemisphere Average (37 studies)
More Summer data than Winter
Non-Refractory Only (doesn’t include metals and elemental carbon)
Sulfate and Nitrate are formed through secondary processes
Organics previously thought of as mostly primary emissions, but that view has changed.
Major Atmospheric Species (fine PM)
Zhang et al., Geophys Res Lett, 2007

## Slide 10: Sources of Atmospheric Aerosols
Meng et al. 1997, Science, 277, 116.
aerosol

## Slide 11: ORIGINS OF ATMOSPHERIC AEROSOL
Soil/dust/Sea salt
Combustion

## Slide 12: Atmospheric Organic Matter: Oxidation state and carbon numbers
oleic acid
ethane
acetaldehyde
phenanthrene
sucrose
levoglucosan
sesquiterpene
monoterpene
isoprene
C5 tetrol
CH2O
glyoxal
glyoxal
dimer
oxalic
acid
pinonic
pinic
C8
triacid
butane
octane
toluene
CH4
CO2
CO
MVK
methyl
glyoxal
fulvic
acid
dodecane
CH3OH
elemental
carbon
Ox. State ≈ 2 (O/C) – (H/C)
Kroll, Nature Chemistry, 2011.
C40

## Slide 13: Chemical complexity of atmospheric organics
carbonyls, alcohols, acids only
Ox. State ≈ 2 (O/C) – (H/C)
C40
Ambient Mass Concentrations Decrease
Kroll, Nature Chemistry, 2011.

## Slide 14: Oxidation state of organic aerosol
Organic aerosol is an intermediate in the oxidation of most organics to CO2
CO2
CO
C40
Kroll, Nature Chemistry, 2011.
Organic Aerosol
gas
particle

## Slide 15
Jimenez, Canagaratna, Donahue, et al., Science, 2009
2D – Volatility Basis Set space
Illustration of SOA evolution through 2D-VBS space

## Slide 16
Secondary Organic Aerosol (SOA) Formation: Example
- 10 days of measurements from thermal desorption aerosol gas chromatograph (TAG)
- PAR = visible light
Naphthalene: C10H8 (mostly in Gas-phase)
Phthalic acid: C8H6O4 (In both Gas- and Particle-phase)
Williams et al., PNAS, 2010
Particle-Phase Concentrations

## Slide 17
Jimenez et al, Science, 2009
Major Chemical Composition of Atmospheric Fine Particulate Matter

## Slide 18
Primary vs Secondary Organic Aerosol (OA)
Zhang et al., Geophys Res Lett, 2007
Effects of organic gases and organic particles can NOT be thought of as separate issues.
Secondary OA > Primary OA

## Slide 19
Observed SOA > modeled SOA
Lack in our fundamental knowledge of SOA formation and transformation.
At least partially due to lack of measurements for semivolatile compounds.
Volkamer et al., Geophys Res Lett, 2006.
Major discrepancy between measured and modeled SOA

## Slide 20
Organics make up 20-90% of fine particle mass and contain tens of thousands of compounds that can be used to determine sources and transformations (much is Secondary).
What we need to know about atmospheric organic matter:
-Physical Properties of Particles
-Chemical Properties
-composition and concentrations (gases and particles)
-composition transformations as air masses age
-Want to determine all sources and fate of atmospheric gases and particles.
-What effects do these particles and gases have on the environment?
-What can be done about it? (Policy and Management)

## Slide 21
Northern Hemisphere Average (37 studies)
More Summer data than Winter
Non-Refractory Only (doesn’t include metals and elemental carbon)
General Speciation: AMS Speciation (PM1)
Zhang et al., Geophys Res Lett, 2007

## Slide 22
Low Volatility Oxygenated Organic Aerosol (LV-OOA)
x%
y%
z%
Semivolatile OOA (SV-OOA)
Hydrocarbon-like OA (HOA)
x, y, z% varies (x > y > z in urban locations, z > y > x in remote locations)
Can also provide estimate of Biomass OA, but some interference exists
Still lacks specifics on sources of OA
Specifics are crucial for Regulation and Modeling Efforts
More Specific: AMS Speciation (w/ PMF of OA)

## Slide 23
TAG
Thermal Desorption Aerosol Gas Chromatograph (TAG)
An in-situ instrument used to study the
Sources and Transformation of Organic Particulate Matter
Hourly measurements of organic aerosol molecular composition
Williams et al., Aerosol Sci Technol, 2006
More Specific Yet: TAG

## Slide 24
1. Collection technique:
  Inertial Impaction (300C)
2. Sample transfer:
  Thermal Desorption (50-3000C)
3. Chemical separation:
  Gas Chromatography
4. Compound identification and quantification:
  Electron Impact Mass Spectrometry
Gas
Chromatograph
Mass
Spectrometer
Heated
valve
Aerosol Collector
&
Thermal
Desorption Cell
Cyclone Precut
(PM2.5)
Humidifier
(adhesion)
Filter
(field blank)
x
1
2
3
4
Note: many particles will be internally mixed.
Factor Analysis
to group compounds

## Slide 25
15.00
20.00
25.00
30.00
35.00
40.00
45.00
0
500000
1000000
1500000
2000000
2500000
3000000
3500000
4000000
4500000
5000000
Time-->
Abundance
TIC: 33702-12.D
TIC: 33702-13.D (*)
Various forms of Petroleum Combustion
Coffee
Residential Wood Combustion
Plant Waxes
Relative Abundance
Retention Time
Secondary Organic Aerosol
Organic portion (20-90% of total mass) is helpful in determining and understanding:
  - Particle sources
  - Particle formation processes
  - Particle transformations
Williams et al., Aerosol Sci Technol, 2006

## Slide 26
Example Sources
Positive Matrix Factorization of Molecular Marker Compounds
Multivariate fit of TAG PMF factors to total OA from AMS
Primary Vehicle Emissions
Food Cooking
Plant Waxes
Biomass Burning:
Softwood
Biomass Burning:
Hardwood
Pesticides
Pharmaceuticals
Anthropogenic Secondary Organic Aerosol (SOA)
Biogenic SOA: Isoprene SOA
Biogenic SOA: Terpene SOA
More Specific Yet: TAG Speciation
(scaling to AMS OA mass)
Plasticizers
Further Aged Anthro-SOA

## Slide 27
Los Angeles
Riverside
N
80 km
San Diego
135 km
PM2.5 Gridded Emissions (short tons/ozone season day/grid cell)
Williams et al., Atmos Chem Phys Discuss, 2010
Example TAG Field Study:
Study of Organic Aerosol at Riverside (SOAR)
Use hundreds of TAG compound timelines in Positive Matrix Factorization (PMF)
Determine major OA components (sources)
Scale TAG factors to AMS OA mass
7/29/2005
7/30/2005
7/31/2005
8/01/2005
8/02/2005
8/03/2005
8/04/2005
8/05/2005
8/06/2005
8/07/2005
8/08/2005
8/09/2005
Vehicle Marker
SOA Marker
TAG’s 1-hour time resolution provides diurnal trends

## Slide 28
Main methods to determine particle sources:
Chemical Mass Balance:
Factor Analysis (e.g., Positive Matrix Factorization):
cik= concentration of chemical species i in the fine particles at receptor site k
aij = relative concentration of species i in the fine particle emissions from source j
sjk = increment to total fine PM concentration at receptor site k originating from source j
m= # of source types
Schauer and Cass, ES&T, 2000
Ulbrich et al., Atm Chem Phys, 2009
X = concentration of chemical species
G = Factor Profile
F = Factor Time Series
E = Residuals
p = Factor#
= estimated errors (uncertainty)
Q = quality of fit parameter
G and F are determined by minimizing sum of least squares between residuals and errors:

## Slide 29
Contribution to Factor (each factor profile sums to 1)
SOA1
SOA2
SOA3
SOA4
+SV
RPA
LV
FC
BB
Bio
Hydrocarbon
Oxygenated
Biogenic
N-Containing
Other
Williams et al., Atmos Chem Phys Discuss, 2010
TAG PMF Components (SOAR)
Biogenic Particles
Biomass Burning
Food Cooking
Local Vehicles
Regional Primary Anthropogenics
Aged SOA + Biogenic SOA
Aged SOA
Regional Fresh SOA
Local Fresh SOA

## Slide 30
Supporting Information
Local Meteorology
Backward Trajectory Modeling
Correlations
RH
Temp
O3
CO
OC/EC
gas-phase organics
AMS species
ATOFMS (single particles)
Etc.

## Slide 31
8.0
6.8 mg m-3
8.6
10.0
13.0
11.6
10.7
10.1
11.7
8.0
5.3
9.5
0:00
2:00
4:00
6:00
8:00
10:00
12:00
14:00
16:00
18:00
20:00
22:00
SOA1
SOA2
SOA3
SOA4+Semivolatile
Regional Primary Anthropogenic
Local Vehicle
Food Cooking
Biomass Burning
Primary Biogenic
Measured OA
Williams et al., Atmos Chem Phys Discuss, 2010
TAG PMF Components (summer)
SOA1 = Local Fresh SOA
SOA2 = Regional Fresh SOA
SOA3 = Aged SOA
SOA4 = Aged SOA + Biogenic SOA
SOA~70% of fine OA
Immediately downwind of large urban area
Previous Studies: SOA~20-50% of fine OA

## Slide 32
Docherty et al., ES&T, 2008

## Slide 33
Spracklen et al., ACPD, 2011
What Models are still missing